## Slide 1
SMART
COASTER
智慧杯墊
START PRESENTATION
M11451001 楊婕
M11451007 楓尹翔
M11451011 簡翊程
M11451027 顏梓淮
M11451029 吳家瑜
TEAM2
1

## Slide 2
01
Hardware
Software
Assignment
02
03
04
05
06
Contents
Topic
System architecture
Bill of materials
2

## Slide 3
01
office worker
When was the last time you took a sip of water?
The Cost of Deep Work
3
Topic
Busyness as the Norm
The Invisible Health Hazard
Have You Had Water Today ?
An Overlooked Office Wellness Problem

## Slide 4
  Manual Entry
  Irrelevant Notifications
4
  High Cost
  Container-Specific
Mobile Apps / Desktop Software
Smart Bottles
Existing
Solutions
Our
Solution
Smart Coaster
  Low Cost
  Zero-Effort Automatic Tracking
  Smart Reminders with LED Light
  Use your existing drinkware
01
Topic

## Slide 5
5
Transport Layer
Physical Layer
Application
Layer
Presentation
Layer
02
System architecture
Session Layer
Data Link Layer
Network Layer
  HX711 + Pressure Sensor Module
  Bakelite board
  LED Light Strips
  Button
  ESP32 Wi-Fi / BLE
  ESP32 Wi-Fi IP Address
  Use BLE packet transmission protocol to transmit sensor data
  ESP32 maintains a session with the Blynk cloud server (Wi-Fi/BLE connection)
  analog → digital
  Format the data and send it to Blynk App
  Display the user interface through the Blynk IoT platform and Arduino IDE program

## Slide 6
6
Hardware
03
1.Weight sensor
2.Perfboard
3.LED Light Strips
4.Button
5.ESP32

## Slide 7
Weight sensor
7
  Model: HX711 + Pressure Sensor Module (5kg)
  Purpose: Amplifies the signal received by the Load Cell and transmits it to the HX711, which converts the analog signal into a digital signal and transmits it to the ESP32.

## Slide 8
Perfboard
8
  Size: 85mm*85mm (900 holes)
  Purpose: To integrate all components

## Slide 9
LED Light Strips
9
  Model: ws2812b
  Size: 24 LEDs, approximately 40cm
  Purpose: To remind customers when it's time to drink or refill their water bottle

## Slide 10
Button
10
  Model: PBS-33B Reset (non-locking) button
  Purpose: Returns the weight of a cup placed on a coaster to zero.

## Slide 11
ESP32
Purpose:
1.Data Acquisition and Control: Receives digital signals (DT/SCK) from the HX711 module, calculates them, and converts them into actual weight (grams/ml of water or beverage).
  Control Output: Based on the calculated results, precisely controls the color, brightness, and dynamic effects of the WS2812B light bar.
  Input Processing: Monitors the status of the PBS-33B button and performs zero reset operations.
11
2. Smart Connectivity: This is the most powerful feature of the ESP32. It can transmit weight and hydration data to a cloud server via Wi-Fi or to a mobile app via Bluetooth (BLE).
3. Logical Operations and State Management: Runs the Arduino program

## Slide 12
04
12
Software －WOKWI
Test the operation and program execution of ESP32 on the development board. Verify the feasibility of the required hardware and software resources to ensure that their specifications and functions fully meet the design requirements.

## Slide 13
04
13
Software －Blynk IoT platform
Functions are shown on the User Interface Display
2025/10/30
water level is insufficient－RED
water level is sufficient－GREEN

## Slide 14
14
Software －Arduino IDE
Record date
Current bottle
weight
Today's water
intake
Reminder to
fill water
ESP32 connect to Wi-Fi
Use a library function to get today's date
Reset the bottle's weight to zero
Measure the bottle's weight
Detect when a drinking event occurs
Add the decreased water amount to today's total water intake
Reset the accumulated water intake to zero at the start of each new day
Use a library function to make the LED light up
If the water weight is below 100g, then turn on the red light
Record today's total water intake to the data table at 23:59
04

## Slide 15
05
numbers | parts | specification | quantity | price (NT) | picture | reference website
1 | weight sensor | Measures the weight of items placed on the coaster to provide data input for intelligent judgment. | 1 | 25 |  | 
2 | bakelite board | As the main structural material of the coaster, it provides a stable and insulating base. | 1 | 25 |  | 
3 | LED light strip | Provides visual feedback to indicate the status of the water volume (e.g., when to drink water , when to refill water ). | 1 | 6 |  | 
4 | botton | Provides a manual input interface for users to reset, power on or off, or switch functions. | 1 | 8 |  | 
5 | ESP32 | The project's core microcontroller is responsible for data processing, Wi-Fi/Bluetooth connections, and controlling all peripheral hardware. | 1 | 255 |  | 
15
Bill of Materials
https://shopee.tw/%E3%80%90%E5%8F%B0%E7%81%A3%E7%89%A9%E8%81%AF%E3%80%9150kg%E7%A7%A4%E9%87%8D%E6%84%9F%E6%B8%AC%E5%99%A8-%E4%BA%BA%E9%AB%94%E7%A7%A450KG%E9%9B%BB%E9%98%BB%E6%87%89%E8%AE%8A%E5%8D%8A%E6%A9%8B%E5%BC%8F%E6%84%9F%E6%B8%AC%E5%99%A8-i.10207300.848013561?sp_atk=cc23c6ce-57ce-474b-a757-35cf7af70ac3&xptdk=cc23c6ce-57ce-474b-a757-35cf7af70ac3
https://shopee.tw/%E3%80%90%E7%A5%A5%E6%98%8C%E9%9B%BB%E5%AD%90%E3%80%91KT-1-SL-1-%E9%9B%BB%E6%9C%A8%E6%9D%BF(900%E5%AD%94)-J-1-%E8%90%AC%E7%94%A8%E6%9D%BF-%E9%9B%BB%E8%B7%AF%E6%9D%BF-PC%E6%9D%BF-PCB-%E6%B4%9E%E6%B4%9E%E6%9D%BF-%E5%AF%A6%E9%A9%97%E6%9D%BF-%E7%B7%9A%E8%B7%AF%E6%9D%BF-i.27742636.5048744441?sp_atk=98ef8bfe-469b-4fb2-8914-00211cf7c015&xptdk=98ef8bfe-469b-4fb2-8914-00211cf7c015
https://shopee.tw/%E8%97%8D%E5%85%89(%E5%8F%AF%E5%AE%A2%E8%A3%BD%E5%8C%96%E9%95%B7%E5%BA%A6)-12V%E9%9C%93%E8%99%B9%E7%87%88%E5%B8%B6%E3%80%90%E6%B2%9B%E7%B4%9C%E5%B0%8F%E9%8B%AA%E3%80%9110%E5%85%AC%E5%88%86%E8%B5%B7%E5%AE%A2%E8%A3%BD-LED%E9%9C%93%E8%99%B9%E7%87%88%E5%B8%B6-i.4984330.23369347953?sp_atk=65264f74-9857-4c6d-8ca7-d6bf685e4b8f&xptdk=65264f74-9857-4c6d-8ca7-d6bf685e4b8f
https://shopee.tw/%E3%80%90%E9%80%A0%E7%89%A9%E4%BA%BA%E3%80%91%E3%80%8A%E5%8F%AF%E7%B5%B1%E7%B7%A8%E3%80%8BArduino-%E6%8C%89%E9%88%95%E6%A8%A1%E7%B5%84-%E6%8C%89%E9%8D%B5%E6%A8%A1%E7%B5%84-%E5%A4%A7%E6%8C%89%E9%8D%B5-%E8%BC%95%E8%A7%B8-%E6%8C%89%E9%88%95-%E6%8C%89%E9%8D%B5%E9%96%8B%E9%97%9C-%E9%AB%98%E9%9B%BB%E5%B9%B3%E8%BC%B8%E5%87%BA-5%E8%89%B2-i.899779.7357690068?sp_atk=877e3880-6198-4137-a94f-e5fc6392c2a1&xptdk=877e3880-6198-4137-a94f-e5fc6392c2a1
https://shopee.tw/%E7%84%A1%E5%90%8D%E7%A7%91%E6%8A%80%E5%8E%9F%E5%BB%A0-ESP32-S3-SUPERMINI-%E9%96%8B%E7%99%BC%E6%9D%BF-Type-c-WIFI-%E8%97%8D%E8%8A%BD-%E7%89%A9%E8%81%AF%E7%B6%B2-i.156997135.26626006239?sp_atk=223d752e-1d51-4703-9d3c-ba48e2fffb3d&xptdk=223d752e-1d51-4703-9d3c-ba48e2fffb3d

## Slide 16
06
M11451001 楊婕 | Bill of materials、Hardware
M11451007 楓尹翔 | GitHub website、Presentation
M11451011 簡翊程 | Software、PPT
M11451027 顏梓淮 | Hardware、PPT
M11451029 吳家瑜 | Purchase、Software、PPT
16
Assignment

## Slide 17
THANK
YOU!
17